## Slide 1: Optimization challenge Configuring autonomous vehicles
Silviu S. Craciunas
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 2: TTTech Key Facts
Copyright © TTTech Computertechnik AG. All rights reserved.
TTTech provides highly reliable and networked electronic systems with solutions based on time-triggered networking technology and modular building blocks for safety controllers
Globally oriented high-tech company, headquartered in Vienna, Austria
20 years of innovation leadership – successful transfer of groundbreaking research from TU Vienna to high-volume production
Chart: TTTech Gross Performance in MEUR
| 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018





MEUR | 17.4 | 22.2 | 29 | 37 | 42.1 | 52.7 | 65.374 | 73.901 | 96.6 | 144.9

## Slide 3: TTTech Group | markests, customers and partners
Copyright © TTTech Computertechnik AG. All rights reserved.
INDUST- RIAL
86+
OFF- HIGHWAY
127+
AERO- SPACE
158+
AUTO- MOTIVE
612+
R&D/ENG/ ADMIN
717+
EMPLOYEES / SUBCONTRACTORS
1,700+
AUSTRIA
GERMANY
USA
SERBIA
CZECH REP.
ITALY
CROATIA
BOSNIA
ROMANIA
FINLAND
CHINA
JAPAN
SPAIN
13
COUNTRIES
HQ 3
2
2
1
1
1
1
1
1
1
1
1

## Slide 4: What do these markets have in common?
Copyright © TTTech Computertechnik AG. All rights reserved.
Boeing 787
Vestas Wind Turbines
Audi Piloted Driving
Prinoth Leitwolf
Thales Railway Signalling
NASA Orion
10/4/19
Reliable networks and safety controls from TTTech

## Slide 5: R&D Funded Projects at a Value of 20 MEUR
Copyright © TTTech Computertechnik AG. All rights reserved.
Strategic R&D of time-triggered communication platforms, prototypes for electronic modules, on-board software and safety platform elements for relevant future application domains
  EC-funded projects in ARTEMIS, DREAMS, ENABLE-S3, ECSEL, ITEA 1&2, Eurostars, Greencars, Cleansky, Marie Currie and other R&D Projects directly funded in FP5, FP6, FP7, H2020
  US programs: NASA, DARPA, NSF
  Aerospace: Airbus, Boeing, Diehl, Honeywell, Liebherr, Safran, Thales, UTC Aerospace Systems etc.
  Automotive: Audi, AVL, Continental, Delphi, Denso, Valeo, Volvo, etc.
  Industrial: Alstom, IBM, Sysgo, Thales Austria, etc.
  Off-Highway: Palfinger, Schwing, etc.
  Semiconductors: ams AG, Infineon, Intel, NXP, ON Semiconductor, etc.
  Universities: Vienna University of Technology, Berkeley University of California, DTU, Chalmers University of Technology, KTH, University of Siegen, University of Kaiserslautern, etc.
  Research Organizations: Austrian Institute of Technology, Barcelona Supercomputing Center, CEA, Technalia, Fortiss GmbH, Fraunhofer Society, SRI, TNO, etc.
R&D Cooperation with Industry
International Research Network

## Slide 6: Autonomous vehicles
Reduced Emission (The use of electric autonomous taxis alone could reduce greenhouse gas emissions by 90% per mile by the year 2030) – Lower Fuel Consumptions
Increase in Safety – Fewer Accidents
Better Health – Less Stress Through Traffic Jams – Much Better Predictability
Less Traffic Jams – Increased Highway Capacity

## Slide 7
Robot
Sense = See
Think = Compute
Act
Brake Actuators
Steering Actuators
Electric Drivetrain
Sensors
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
An autonomous vehicle can be understood as a robot

## Slide 8
Environment camera
Laser scanner
Ultrasound sensors
Stereo camera
Front camera
Radar
Lidar
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
Sensors deployed today

## Slide 9
Source: Motovis
Scene segmentation based on „Deep Learning“ (Neural networks)
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
Sensing, computing and actuating

## Slide 10
Source: Mobileye
Object recognition
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
Sensors deployed today

## Slide 11
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
Modern autonomous vehicles
Traditional approach based on distributed ECUs and separated domains, interconnected through different technologies (ETH, CAN, FlexRay)
Source: Ernst et al. - Ethernet as Future Automotive Communication Backbone

## Slide 12
              Rapid growth of software functionality and the necessary compute performance cannot be addressed with current electronics architecture and ECUs
        autonomous driving
        connectivity
        infotainment
        electrification & hybrids
        new mobility
              Too many ECU’s with too little processing power and memory
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
Modern autonomous vehicles – issue I

## Slide 13
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
Modern autonomous vehicles – issue II
Limitation of the domain concept
N domains imply N times development cost.
N domains imply N times the execution of basic software functions (operating systems, diagnostics, management, etc.)
N domains imply N times sources of software and hardware faults.
N domains imply N times maintenance cost.

## Slide 14
A failure can occur in an arbitrary complex situation.
  Minimum system safety reaction: stop in a safe area or let driver take over – requires > 10 seconds of complex behavior (360 meters at highway speed!).
              Redundancy (active / fallback) to cope with HW and SW failures.
              Make sensor set available to active and fallback systems.
              Provide sufficient computation power also on fallback system.
              Avoid simultaneous failure of active and fallback systems at all cost!
The domain concept is not sustainable for L4/L5 autonomous driving.
Autonomous driving functions require the integration of cross-domain information and functions.
E.g., highly precise maps, sensor fusion
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
Modern autonomous vehicles – issue III
Fail-operational requirement for level 4 autonomous driving

## Slide 15: From distributed, separate ECUs …
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 16: … to a central, integrated platform.
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 17: Integrated platform
Copyright © TTTech Computertechnik AG. All rights reserved.
In Car Computing Platform (ICCP):
- from hardware to software
- from distributed to centralized
Infotainment
Gateway
Autonomous driving

## Slide 18: Integrated platform
Copyright © TTTech Computertechnik AG. All rights reserved.
Safety core
Performance core
Special purpose core (GPU, NPU, etc.)
Storage
Networked I/O
ICC Network & uplink
Memory
ICCP – Shared HW resources
App
App
App
App
App
App
App
App
App
App
App
App
ASIL
QM
Consumer
Production resource allocation
OTA updates
cloud services
OTA diagnostics/
data collection
HW upgrade
A
p
pp
App
Ap
p
App
Ap
Ap
Ap
App

## Slide 19: ICCP – Foundational Technology Principles
Copyright © TTTech Computertechnik AG. All rights reserved.
Layered distributed computer system: SoC layer, PCB layer, ECU layer, Vehicle layer.
Virtualization on all four layers of all ICCP resources: processors, communication, storage.
Static configuration/scheduling for safety and security.
Dynamic configuration/scheduling for performance, flexibility, maintainability, upgradeability.
Safety first – static trumps dynamic.

## Slide 20: RazorMotion
Copyright © TTTech Computertechnik AG. All rights reserved.
  Processing Resources: 1x Renesas RH850P/1H-C (ASIL D MCU with lockstep cores @ 240MHz) 2x Renesas R-Car H3 (ASIL B SoC with 4x Cortex A57, 4x Cortex A53, 1x Cortex R7, 1x IMP-X5, 1x IMG GX6650 GPU)
  Video Interfaces: 12 x camera inputs (GMSL) incl. remote supply (PoC) 2 x display outputs (FPD-Link III)
  Communication Interfaces: 4x OABR 100BASE-T1 2 x FlexRay (A/B channel) – wakeup capable 2 x HS-CAN – wakeup capable 4 x CAN-FD 2 x LIN I/O Interfaces 2 x analog/digital inputs 2 x high side outputs 1 x sensor supply output (5V)

## Slide 21: MotionWise
Copyright © TTTech Computertechnik AG. All rights reserved.
  Integrated multi-SOC platform, instead of separate platforms (Classic Autosar, Adaptive Autosar, plain POSIX) for each host
  Guaranteed realtime processing (vs. Adaptive Autosar does not have a realtime concept)
  Deterministic scheduling and guaranteed end-to-end latency control across heterogeneous SoCs
  Integrated automotive services across multi-SoC platform (diagnostics, flashing/update, calibration, …)
  Seamless application portability across heterogeneous SoCs
  Integrated communication and data framework across heterogeneous SoCs, including persistent storage

## Slide 22: ICCP Platform
Copyright © TTTech Computertechnik AG. All rights reserved.
Deterministic Ethernet / PCIe Backbone
Task1
Task2
Task3
Task4
…
Taskn
Autosar OS
Safety RTOS
Linux
Multi-Core MCU
Safety
Performance/Safety
Performance
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
GPU
CPU
CPU
CPU
CPU
MiddleWare
Different multi-core CPUs:
process the information arriving from a variety of sensors (radar, ultrasonic sensors, cameras, LIDAR, etc.)
run control loops
run other utility functions (lane keeping/changing assistant, emergency braking, logging, etc.)
ICCP = Heterogeneous multi-core multi-SoC platform featuring a variety of CPUs and GPUs running at different speeds, which are interconnected through either a deterministic Ethernet backbone (TSN) or through PCIe

## Slide 23: ICCP platform – software stack
Copyright © TTTech Computertechnik AG. All rights reserved.
Each host can run a different operating system depending on the safety and performance requirements.
Each such OS can have a different scheduling policy, ranging from fixed-priority (AUTOSAR) to table-driven or dynamic priority scheduling (SafetyRTOS).
On top of this platform a large number of different software functions, implemented by different vendors, must be integrated and deployed.
The system is composed of applications (called tasks or runnables), that are either pre-assigned to cores or must be assigned by the scheduling algorithm.
Tasks have real-time requirements, both in terms of execution (offset, deadline, jitter) as well as temporal dependencies arising from either task chains or communication between tasks.

## Slide 24: ICCP problem
Copyright © TTTech Computertechnik AG. All rights reserved.
Function (task) allocation and scheduling problem
The allocation of functions (or even their partitioning) to the layers of ICCP that determines which resources (memory, communication, computation, etc.) are to be assigned to which functions (and at which points in time).
3 types of allocation/scheduling:
fully-static offline (table-driven/time-triggered)
dynamic-offline (i.e. mode change)
dynamic-online
Different dimensions to the allocation problem:
Assignment of tasks to cores/CPUs
Scheduling of tasks in the Guest OS
Communication backbone
NP-complete

## Slide 25: Time-triggered systems
Copyright © TTTech Computertechnik AG. All rights reserved.
Time-triggered vs. event-triggered systems: transportation example
Taxis are event-triggered: they go whenever they are needed/called - very flexible
Trains are time-triggered: they run according to a fixed schedule – very predictable

## Slide 26: Deterministic time-triggered design
Event triggered system
Disadvantages:
  Realtime behaviour can not be guaranteed
  Additional applications impact overall system behaviour
Benefits:
  Realtime behavior guaranteed
  Deterministic integration behaviour „composability“
  Freedom-from-Interference behavior
Supporting features:
  „Remaining time“ to be able to fully load WCET
  Smart scheduling mechanisms („Hybrid schedule“)
  QM background tasks do not influence critical timing
System Load
100%
70%
Runtime variation in each task
To be adressed by reserving min. 30% system performance
System Load
100%
70%
Runtime variation in each task considered in WCET
System can be loaded to 100%
Deterministic (time-triggered) system
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
Notes: Why there is the same amount of apps running on event triggered system as on the TT system – NO of applications??
White parts shooudl be coloured

## Slide 27: Preemptive vs. non-preemptive scheduling
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
Preemptive scheduling allows a running task to be interrupted by another task, whereas in non-preemptive scheduling, the running task hast to complete or voluntarily yield for other tasks to be able to run
time
0
time
0
deadline miss
In static time-triggered scheduling, preemption means that we can split a task in multiple pieces in order to better utilize the timeline
Notes: Why there is the same amount of apps running on event triggered system as on the TT system – NO of applications??
White parts shooudl be coloured

## Slide 28
Challenge #1

## Slide 29: Challenge 1 – function allocation
Copyright © TTTech Computertechnik AG. All rights reserved.
Platform
m CPUs defined by:
  # of cores
  speed (cores have the same speed)
  macrotick
Table-driven scheduling
Preemption: yes
Migration: no

## Slide 30: Challenge 1 – microtick vs macrotick
Copyright © TTTech Computertechnik AG. All rights reserved.
time
0
Theoretical timeline is infinitely divisible (Planck time ~ 5.4 × 10−44 seconds)
Microtick - Ticks generated by the physical oscillator of a clock
Macrotick - Multiple of Microtick chosen by designer of clock/system
microtick
macrotick

## Slide 31: Challenge 1 – macrotick vs system overhead
Copyright © TTTech Computertechnik AG. All rights reserved.
Trade-off between schedulability and overhead/scheduler runtime

## Slide 32: Challenge 1 – function allocation
Copyright © TTTech Computertechnik AG. All rights reserved.
Tasks - n tasks defined by:
  Id : Integer
  UniqueName : A unique name for the task
  BCET : Best Case Execution Time of the task; in microseconds
  WCET : Worst Case Execution Time of the task; in microseconds; Execution time of a task is between BCET and WCET
  Period : Period of a task in microseconds
  Deadline : Deadline of a task in microseconds
  EarliestActivation : The earliest activation time of task within its period in microseconds.
  MaxJitter : Maximum Jitter in microseconds that the task can have. -1 for no jitter limitations.
  Offset : The initial displacement of the task arrival times in microseconds.
  DeadlineAdjustment : The deadline limit for an instance of a task in microseconds. The limit can not be greater than (Deadline - EarliestActivation).
  CpuId : Id of the assigned CPU. Must be assigned.
  CoreId : Id of the assigned Core of the CPU; optional; -1 for no core assignment.

## Slide 33: Challenge 1 – activation, deadline, period
Copyright © TTTech Computertechnik AG. All rights reserved.
time
0
WCET
activation
deadline
period

## Slide 34: Challenge 1 – hyperperiod and preemption
Copyright © TTTech Computertechnik AG. All rights reserved.
time
0
Hyperperiod = lcm of all periods
2 out of 4
1 out of 6
4
6
8
12

## Slide 35: Challenge 1 – jitter
Copyright © TTTech Computertechnik AG. All rights reserved.
Jitter*
Jitter = Jitter* - WCET
0
5
10
10
15
20
30
35
40
20
25
30
WCET

## Slide 36: Table-driven static scheduling
Copyright © TTTech Computertechnik AG. All rights reserved.
Periodic hard real-time tasks with (WCET, Period) definition
Are pre-assigned to CPUs (WCET is already scaled to speed)
Can be pre-assigned to core, if not assigned, assignment will be part of the allocation and scheduling problem
Can have deadline, activation, jitter constraints
Preemption is allowed, migration is not allowed
The result of the scheduling algorithm is an
assignment of tasks to cores and for each core a
static table which determines the exact timely
behavior of assigned tasks

## Slide 37
Challenge #2

## Slide 38: Challenge 2 – adding task dependencies
Copyright © TTTech Computertechnik AG. All rights reserved.
Characteristic of automotive software – Cause-effect chains:
provide additional timing and dependency requirements on the execution of tasks
can span across multiple activation patterns
include multiple tasks, even the same task multiple times
have priorities and end-to-end latencies
include communication latencies
Source: Becker et al. - Synthesizing Job-Level Dependencies for Automotive Multi-rate Effect Chains

## Slide 39: Challenge 2 – adding task dependencies
Copyright © TTTech Computertechnik AG. All rights reserved.
Scheduling problem:
Schedule tasks such that the chain dependencies are fulfilled (next slide)
Schedule tasks in such a way that all chains are fulfilled in terms of their end-to-end latencies
Optimize such that chains with higher priority have a lower latency than those with lower priority
For now we consider that communication delays are fixed (PCIe)

## Slide 40: Dependency chains
10
20
30
40
0
Latency 2
Latency 1
τ1
τ2
τ3
τ4
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 41: Challenge 2 – adding task dependencies
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 42: Challenge 1+2 – example approach based on EDF
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 43: Optimal vs. non-optimal
Optimal schedule
Search space
Solution space
Near-optimal solution space
Optimal Solution
Optimal scheduler
Looks at entire search space
Finds a solution if there is one (might take a long time)
If no solution is found, no other algorithm can find a solution
Typically NP-complete
Heuristic scheduler
Looks at a fraction of the search space
Not guaranteed to find a solution
Designed to be fast
Tries to find near-optimal solution
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 44: Important scheduling results
Earliest-Deadline-First [Liu73]
dynamic scheduling algorithm
at each time instant, the job with the earliest relative deadline is chosen to run
preemptive and non-preemptive variants
optimal and non-optimal results depending on task properties (presented next)
Rate-Monotonic [Liu73]
static scheduling algorithm
static priotities are inverse proportional to period lengths
optimal among fixed-priority algorithms (periodic tasks)
sufficient and necessary schedulability condition exist
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 45: EDF scheduling
Assumption
The task set is schedulable such that all jobs meet their relative deadlines iff
For RM the test is only sufficient and utilization bound is smaller
[Liu73]
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 46: EDF Scheduling
Assumption
Simple approach
only sufficient
0
4
8
12
16
20
24
0
4
8
12
16
20
24
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 47: Processor demand
0
4
8
12
16
20
24
0
4
8
12
16
20
24
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 48: EDF simulation
Copyright © TTTech Computertechnik AG. All rights reserved.
We can use the necessary and sufficient schedulability test based on dbf
We can use it to generate a static schedule table – simulate EDF until 2*Hyperperiod + max_offset
Schedulability test:
Two knobs to play around with: offset and deadline of each task

## Slide 49: Simulated Annealing + EDF simulation
Copyright © TTTech Computertechnik AG. All rights reserved.
Simple Algorithm:
Generate initial candidate:
task offsets = 0
task deadlines = Period
task to core assignment based on best-fit/first-fit
Simulated Annealing Loop:
EDF schedulability test/EDF simulator
Build dependency graph (next slide)
Chain latency test (linear)
Generate neighbor: modification of offsets/deadlines (what is a good metric?)

## Slide 50: Checking task chains
Copyright © TTTech Computertechnik AG. All rights reserved.
Open questions/things to improve:
Good metrics (task assignment)
Can we cover the whole solution space with a subset of offset/deadline assignments?
Do we need multiple offsets per task?
Can we encode jitter requirements?
Better GenerateNeighbour function?
Scalability?

## Slide 51
Challenge #3

## Slide 52
Copyright © TTTech Computertechnik AG. All rights reserved.
Challenge 3 – adding the network layer
Can be solved as an individual challenge (TSN network scheduling)

## Slide 53: Technology: TTEthernet / TSN
Deterministic Ethernet / PCIe Backbone
Task1
Task2
Task3
Task4
…
Taskn
Autosar OS
Safety RTOS
Linux
Multi-Core MCU
Safety
Performance/Safety
Performance
CPU
CPU
CPU
CPU
CPU
CPU
CPU
CPU
GPU
CPU
CPU
CPU
CPU
MiddleWare
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 54
1s
maximum latency = 4s
T=
0
1
2
3
4
5
0
1
2
3
4
bob
alice
mike
lea
michelle
ana
tim
sam
Experiment
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 55: Priority switch
Copyright © TTTech Computertechnik AG. All rights reserved.
Port A (ingress)
Port B (ingress)
Port C (egress)
Switching fabric
Priority filter
Priority 8
Priority 7
Priority 6
Priority 1

## Slide 56: Priority (AFDX) approach
Copyright © TTTech Computertechnik AG. All rights reserved.
Assign priorities to messages
Latency analysis
Latencies are not fulfilled
NO
YES
Result
Add or change messages

## Slide 57: The TSN/TTEthernet alternative
Copyright © TTTech Computertechnik AG. All rights reserved.
Sending and receiving of frames is done according to a global schedule.
time
0
Correct by design (schedule construction)
Compositional (adding flows can be done incrementally)
Minimal jitter and delay bounds
Devices must have a common understanding of time.

## Slide 58: Network view
Time-triggered communication & timing checks in a network with forwarding: global schedules & delays apply
…switch
…end system
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
I will transmit at time 10 ms
I will accept only between 9 and 11 ms
I will forward at 12 ms
I will forward at 14 ms
I will accept only between 11 and 13 ms
I will expect the message between 13 and 15 ms

## Slide 59: TTEthernet switch
Copyright © TTTech Computertechnik AG. All rights reserved.
Port A (ingress)
Port B (ingress)
Port C (egress)
Switching fabric
Buffer
Priority 8
Priority 7
Priority 6
Priority 1
+

## Slide 60: TSN (Qbv) switch
Copyright © TTTech Computertechnik AG. All rights reserved.
Port A (ingress)
Port B (ingress)
Port C (egress)
Switching fabric
Priority filter
+
Priority 8
Priority 7
Priority 6
Priority 1
t=0 occoccoc
t=1 oocooccc
t=5 cccccccco
t=7 ococcccc
……
Gate Control List

## Slide 61: TSN (Qbv) switch
Copyright © TTTech Computertechnik AG. All rights reserved.
T=
1
2
3
4
0
5
Port A (ingress)
Port B (ingress)
Switching fabric
Priority filter
+
Port C (egress)
Priority 8
Priority 7
Priority 6
Priority 1

## Slide 62: TSN IEEE 802.1 sub-standards overview
Copyright © TTTech Computertechnik AG. All rights reserved.
Provides guaranteed communication latency for time-critical traffic over standard Ethernet even in a converged infrastructure.
Profile of IEEE 1588v2 for synchronization of clocks in the network. Supports timing requirements for scheduled TSN networks.
IEEE 802.1AS
Time Synchronization
IEEE 802.1Qbv
Scheduled Traffic
IEEE 802.1Qcc
SRP Enhancements
IEEE 802.1Qch
Cyclic Queuing and Forwarding
IEEE 802.1Qbu
Frame Preemption
IEEE 802.1Qca
Path Control and Reservation
Allows for optimal bandwidth utilization of non-scheduled background traffic sent in parallel with scheduled traffic.
Defines cycles for forwarding queued traffic using 802.1Qci to assign buffers and 802.1Qbv to shape traffic.
Defines the interfaces for configuration (distributed and centralized) of TSN networks. Supports configuration models for dynamic scheduling of TSN.
Protects against faulty and/or malicious endpoints and switches. Isolates faults to specific regions in the network.
Allows for optimal bandwidth utilization of non-scheduled background traffic sent in parallel with scheduled traffic.
IEEE 802.1CB
Seamless Redundancy
IEEE 802.1Qcr
Asynchronous Traffic Shaping
IEEE 802.1Qci
Filtering and Policing
Protects against faulty and/or malicious endpoints and switches. Isolates faults to specific regions in the network.
Provides bounded latency and jitter (lower performance levels) without time-synchronization.
IEEE 802.1Qcw
YANG Model for Qbv, Qbu, Qci
IEEE 802.1Qcp
YANG Model for Bridging
Extends capabilities of 802.1Qcp to communication of scheduling, preemption and policing configuration date between bridges in combination with NETCONF
Enables communication of basic bridging configuration data between bridges in combination with NETCONF
IEEE 802.1CBcv
YANG Model for CB
Extends capabilities of 802.1Qcp to communication of redundancy configuration date between bridges in combination with NETCONF

## Slide 63: What is a Time-Sensitive Network (TSN)
Copyright © TTTech Computertechnik AG. All rights reserved.
Time Sensitive Networking covers a set of Ethernet sub-standards currently defined in the IEEE 802.1 TSN task group
At the heart of TSN are mechanisms that provide time synchronization for networked devices and scheduled forwarding of defined traffic flows through the network.
Through time synchronization and scheduling, TSN delivers deterministic communication over standard Ethernet, thereby enabling the convergence of critical control traffic with data traffic over one infrastructure without the need for gateways or proprietary solutions.

## Slide 64: Time-Sensitive Network (TSN)
Copyright © TTTech Computertechnik AG. All rights reserved.
IEEE TSN task group - collection of sub-standards that enhance 802 Ethernet with real-time capabilities
Standard | Description
802.1ASrev | Timing & Synchronization
802.1Qbv | Enhancements for Scheduled Traffic (Timed Gates for Egress Queues)
802.1Qbu | Frame Preemption
802.1Qca | Path Control and Reservation
802.1Qcc | Central Configuration Management
802.1Qci | Per-Stream Time-based Ingress Filtering and Policing
802.1CB | Redundancy, Frame Replication & Elimination

## Slide 65: Functional parameters
Copyright © TTTech Computertechnik AG. All rights reserved.
Device capabilities
Queue configuration
Scheduled Es
Scheduled Sw
Scheduled Es+Sw
Critical traffic assigned to the scheduled queues
Non-critical traffic assigned to priority queues (post-analysis through network calculus [Frances@ERTS06])
Isolation: non-critical streams may interfere with each other in priority queues, but not with critical streams (isolated in the scheduled queues)

## Slide 66: 802.1Qbv configurations
Copyright © TTTech Computertechnik AG. All rights reserved.
Only critical traffic (serialized similar to bus systems)
Legacy AVB systems that require a few additional high-criticality flows [Specht@ECRTS16]
Maximize solution space for critical traffic, non-critical traffic can be scheduled by inverting the cumulated schedule of scheduled queues
High-criticality applications that feature both scheduled and non-scheduled traffic, trade-off between schedulability of critical traffic and timeliness properties and flexibility for non-scheduled traffic
Standard AVB (IEEE 802.1BA) network in which flows are serviced according to the priority

## Slide 67: Network and traffic model
Copyright © TTTech Computertechnik AG. All rights reserved.
multi-hop layer 2 switched network via full-duplex multi-speed links
(multicast) TSN streams with multiple frames per stream
communication is from one sender to one or multiple receivers
synchronised time (<1 usec precision)
wire and device delays
Scheduled 802.1Qbv-compatible devices (Sw + Es)
Scheduled (mutually exclusive) & priority queues
Guaranteed delivery of critical traffic with known latency, small & bounded jitter

## Slide 68: TSN schedule
  TSN Switch
  TSN End System
Sender
Receiver 1
Receiver 2
Offline scheduling
  The TSN (Qbv) schedule defines open and close events for the Gate Control List (GCL) in each output port of every TSN device in the network
  The schedule is build off-line taking into account the maximum end-to-end latency, frame length, as well as constraints derived from resources and physical limitations.
  The schedule must enforce a deterministic behaviour of frame transmission and reception
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 69: TSN schedule synthesis
Scheduling for TSN therefore means:
Find transmit (and implicitly receive) times and queue assignment for all frames on all devices such that
  No collisions on ports occur
  Frames are sent correctly in the time domain
  End-to-end latencies are fulfilled
  Other user-defined constraints are fulfilled
  Etc.
Copyright © TTTech Computertechnik AG. All rights reserved.
Schedule correctness conditions
Technology
Communication
User-defined

## Slide 70: Correctness conditions
Frame placement within period
Copyright © TTTech Computertechnik AG. All rights reserved.
time
0
time
0
period
frame size
release
deadline

## Slide 71: Correctness conditions
Copyright © TTTech Computertechnik AG. All rights reserved.
time
0
Frames are not allowed to overlap in the time domain
period = 4
period = 6
Hyperperiod = 12

## Slide 72: Correctness conditions
Copyright © TTTech Computertechnik AG. All rights reserved.
time
0
Frames are not allowed to overlap in the time domain
period = 4
period = 6
Hyperperiod = 12
For all frames scheduled on the same link
check overlapping in any period instance
until hyperperiod of the two considered periods

## Slide 73: Virtual link constraints
Copyright © TTTech Computertechnik AG. All rights reserved.
time
0
time
0
A frame must be received before it is forwarded
Device i
Device i+1
δtransmission
δforwarding
δtransmission = Wire Delay + Port delays + Transmission delay + Precision
δforwarding = Switch forwarding delay

## Slide 74: Correctness conditions
Copyright © TTTech Computertechnik AG. All rights reserved.
time
0
Memory buffer constraints
Maximum allowed time for frame to be stored in switch buffer
Device i

## Slide 75: Correctness conditions
Copyright © TTTech Computertechnik AG. All rights reserved.
time
0
Maximum end-to-end latency constraint
Sender
time
0
Switch 1
time
0
Switch 2
time
0
Receiver
End-to-End Latency

## Slide 76: User constraints
  Scheduling constraints are additional conditions on the correctness of the schedule.
  Start time constraint
  End time constraint
  End-to-end latency constraint
  Transmission gap constraint
  Precedence constraint
  Floating window constraint
  Best-effort reservation constraint
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 77: Transmission Gap Constraint
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
time
0
Enforce a gap between the reception of one flow and the transmission of another
Switch
time
0
Receiver
time
0
Switch
Transmission Gap

## Slide 78: Queue interleaving
Copyright © TTTech Computertechnik AG. All rights reserved.
In order to maintain jitter and latency requirements we expect at each device a certain timely order of frames

## Slide 79: Queue Interleaving
Copyright © TTTech Computertechnik AG. All rights reserved.
synchronization errors, frame loss, time-based ingress policing (e.g. IEEE 802.1Qci) may lead to non-deterministic placement in queues during runtime
timed gates control events on the egress port, not the order of frames in the queue
placing of frames in the scheduled queues at runtime may be non-deterministic
Timely behaviour of streams may oscillate, accumulating jitter for the overall end-to-end transmission
expected

## Slide 80: Queue Isolation
Copyright © TTTech Computertechnik AG. All rights reserved.
Solves the non-determinism problem but reduces the solution space
expected

## Slide 81: Stream (Flow) Isolation
Copyright © TTTech Computertechnik AG. All rights reserved.
Once a flow has arrived, no other flow can arrive in the same queue until the first flow has been completely sent
Better than queue isolation but still restrictive
expected
0
0
t2
t1
t1
t1

## Slide 82: Frame Isolation
Copyright © TTTech Computertechnik AG. All rights reserved.
Ensure that there are only frames of one flow in the queue at a time
Frames from another flow may only enter the queue if the already queued frames of the initial flow have been serviced
Less performant than stream isolation since the solver has to consider at all frame interleavings
expected

## Slide 83: 802.1Qbv scheduling constraint
Copyright © TTTech Computertechnik AG. All rights reserved.
The constraint for minimum jitter scheduling of critical traffic for 802.1Qbv networks is:
isolate frames/streams in the time domain
OR
isolate streams in different queues

## Slide 84: Scheduling problem
Copyright © TTTech Computertechnik AG. All rights reserved.
802.1Qbv
frame constraints
link constraints
stream constraints
end-to-end latency constraints
stream or frame isolation
find routes, offsets and queue assignment for individual frames of
TSN streams from sender to receiver(s) that conforms to the constraints
NP-complete

## Slide 85: TSN correctness constraints
Copyright © TTTech Computertechnik AG. All rights reserved.
Silviu S. Craciunas, Ramon Serna Oliver, Martin Chmelik, and Wilfried Steiner Scheduling Real-Time Communication in IEEE 802.1Qbv Time Sensitive Networks In Proc. 24th International Conference on Real-Time Networks and Systems (RTNS), 2016.
http://www.cs.uni-salzburg.at/~scraciunas/pdf/conferences/craciunas_rtns16.pdf

## Slide 86
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
The question is now, how do we generate such a correct schedule?
How complex is the schedule generation? Can we do it efficently?
We have seen what constitutes a correct schedule.

## Slide 87: SMT/OMT-based scheduling
Formalization of technology, communication and user constraints
Optimal scheduler
Feasible/Optimal schedule
Easily extendable for new constraints
A lot of solvers and a very active community
satisfiability of logical formulas in first-order formulation
background theories
variables
logical symbols
non-logical symbols
quantifiers
Satisfiability Modulo Theories
optimization criteria: Optimization Modulo Theories [Bjørner@TACAS15]
Copyright © TTTech Computertechnik AG. All rights reserved.
OpenSMT [Bruttomesso@TACAS10]
CVC4 [Barrett@CAV11]
Yices [Dutertre@CAV14]
Z3 [de Moura@TACAS08]

## Slide 88: Optimization
Copyright © TTTech Computertechnik AG. All rights reserved.
Optimize schedule with respect to certain properties
of the system (e.g. minimize end-to-end latency of
selected streams)
802.1Qbv-specific optimizations:
QoS properties: minimize required scheduled queues in order to increase QoS properties of non-critical traffic
Design space exploration in case of infeasible use-cases, i.e. find the minimal number of queues required for scheduled traffic such that a schedule is found
Many more optimization opportunities in combination with other TSN sub-standards (e.g. frame preemption)

## Slide 89: Evaluation
Copyright © TTTech Computertechnik AG. All rights reserved.
time
topology
macrotick
link/CPU utilization
size of network
?
periods
hyperperiod

## Slide 90: Experiments
Copyright © TTTech Computertechnik AG. All rights reserved.
Z3 v4.4.1 solver (64bit) (Yices v2.4.2 with quantifier-free linear integer arithmetic)
64bit 4-core 3.40GHz Intel Core-i7 PC with 4GB memory
3 predefined topologies ranging from 3 end-systems connected to one switch to 7 end-systems connected through 5 switches via 1Gbit/s links with a 1usec macrotick granularity (generate high utilization on the links)
Time-out value for a run to 5 hours
System configuration:
Scalability and schedulability experiments

## Slide 91: Scalability experiments
Copyright © TTTech Computertechnik AG. All rights reserved.
Frame isolation method (using an incremental backtracking algorithm with step size of 1)
Vary the problem set in 3 dimensions:
  topology size,
  number of flows,
  flow periods (chosen randomly from 3 sets of predefined periods)
Data size uniformly between 2 and 8 MTU-sized frames
Senders and receivers are chosen randomly

## Slide 92: Scalability experiments
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 93: Scalability experiments
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 94: Scalability experiments
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 95: Frame vs. Stream Isolation
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 96: Schedulability experiments
Copyright © TTTech Computertechnik AG. All rights reserved.
Generated inputs that force streams to interleave if scheduled in the same egress queue
Runs w/ and w/o optimization objectives using both stream and frame isolation methods
Minimize accrued sum of the number of queues used per egress port
No incremental steps for optimization runs

## Slide 97: Schedulability experiments
Copyright © TTTech Computertechnik AG. All rights reserved.

## Slide 98: Heuristics
Copyright © TTTech Computertechnik AG. All rights reserved.
Greedy Randomized Adaptive Search Procedure (GRASP)-based metaheuristic together with M. L. Raagaard and P. Pop (c.f. [Raagaard])
For large networks we have to use heuristics, e.g:

## Slide 99: Conclusion
Copyright © TTTech Computertechnik AG. All rights reserved.
Challenge #1 : allocate task to cores and create a table-driven schedule for tasks running on a ICCP platform such that the simple real-time constraints are fulfilled
Challenge #2 : extend the scheduling and allocation problem from #1 such that complex task chains are also fulfilled
Challenge #3 – Variant 1: extend the allocation and scheduling problem from #2 such that the deterministic communication backbone is considered, i.e., also schedule a simple TSN network
Challenge #3 – Variant 2: solve the TSN scheduling problem separately but consider really large networks with hundreds/thousands of nodes/streams

## Slide 100: References
Copyright © TTTech Computertechnik AG. All rights reserved.
Most papers can be found at http://www.cs.uni-salzburg.at/~scraciunas/ or directly from Paul
See reading list from Paul
S.S. Craciunas, R. Serna Oliver, M. Chmelík, and W. Steiner - Scheduling Real-Time Communication in IEEE 802.1Qbv Time Sensitive Networks. In Proc. RTNS 2014
M.L. Raagaard, P. Pop, S.S. Craciunas - GRASP-based Gate-Control List Synthesis for IEEE Time-Sensitive Networks (TSN). (to be published)
P. Pop, M.L. Raagaard, S.S. Craciunas, and W. Steiner - Design Optimization of Cyber-Physical Distributed Systems using IEEE time-sensitive Networks (TSN). IET Cyber-Physical Systems: Theory & Applications 1, 1 (2016), 86–94.

## Slide 101
Vienna, Austria (Headquarters) | USA | Japan | China
Phone +43 1 585 34 34-0 office@tttech.com | Phone +1 978 933 7979 usa@tttech.com | Phone +81 52 485 5898 office@tttech.jp | Phone +86 21 501529250 china@tttech.com
www.tttech.com |  |  | 
Copyright © TTTech Computertechnik AG. All rights reserved.
Notes: altbacken

## Slide 102: Shuffling and media reservation
October 4, 2019
Copyright © TTTech Computertechnik AG. All rights reserved.
Port A (ingress)
Port B (ingress)
Port C (egress)
Switching fabric
Buffer
Priority 8
+
Priority 7
Priority 6
Priority 1
Priority 8 - PCF
Priority 7 - TT
Priority 6 - RC High
Priority 1 -- 4 - BE
Priority 5 - RC Low